An Experimental and Theoretical Study

on the Accuracy of Experimental Methods

Through Mathematical Modeling

of Cell Capacitance in Multi-compartment Cells

Christopher Khalil

Department of Biomedical Engineering,

New Jersey Institute of Technology

cjk4@njit.edu

I. Abstract

It has been observed that the measurement methods for capacitance in the cell membranes of neurons produce an order of magnitude difference within Cancer borealis neuron cells.  We believe that this difference is due to the geometry of the branching nature of neurons.  The three methods of measurement (Current Step, Voltage Clamp, and Voltage Ramp) have been mathematically modeled and were simulated with differing parameters imitating different morphologies of the neuron.  The data shows that the branching nature does significantly contribute to the error seen among the different methods, but more importantly the data reveals that the Current Step method is the most accurate method of measurement of the three, because of its independence of the morphology of the neuron.

II. Introduction

Countless experiments and modeling studies call for knowing what the capacitance values of cell membranes are for the cells being studied.  Because the membrane capacitance is directly proportional to the surface area, experimenters are able to determine the properties of the cell that relate to the surface area.  Since capacitance is a fundamental cell property, it is extremely important that a universal method is utilized so capacitive measurements are routinely attained across many different experiments and studies.

Cell membranes contain resistive and capacitive properties that affect the functioning of the cell.  Knowing this, scientists are able to measure these properties through different methods.  Currently there are three well-known methods that are used to measure the capacitive and resistive properties of the cell: the Current Step, Voltage Step, and Voltage Ramp method.  In principle, all three methods should provide the same capacitive value independent of the method of measurement, but there is an order of magnitude difference seen among the three methods.  Therefore, there is a dissonance between different experiments and the different methods of measurement.  There seems to be very little literature available on this issue.

In attacking the problem, the Stomatogastric Nervous System of the Crab, Cancer borealis, was used because of its accessibility, the use of several innovative techniques to accurately measure cell properties, and the abundance of research already accumulated on it (Nusbaum & Beenhakker 2002).  The neurons of the Cancer borealis are also bigger than most other animal neurons and therefore much easier to impale and record measurements.

It is our hypothesis that the differing of the measurements per method is due to the branching nature of the neurons and therefore the branching contributes differently to each method.  Each method in theory, measures the capacitance but it does not take the branching into consideration.  All three methods were designed and developed on the premise of isopotential cells: cells that have the same voltage throughout the cell.

For this study, we retrieved experimental data by taking intracellular recordings from the Stomatogastric Nervous System using the three methods of measurement.  Afterwards several mathematical models were created and verified by the parameters of the experimental data.  Once the validity of the mathematical models was established, different parameters were altered concerning the geometry of the neuron to observe their affect on the capacitive measurements of the cell membrane.

After analyzing our results, we found that the Current Step method provided the most accurate results compared to the Voltage Step and Voltage Ramp methods.  Through our finding, the Current Step consistently provided the most accurate results as different parameters of the cell neuron were changed.  For the most part, the Current Step method was independent of the cell morphology.  Our data shows that the Current Step method is the best method for retrieving the capacitive value of the cell membrane.

III. Methods

Cell Membrane as a Circuit

Figure 1: The representation of the cell membrane as an equivalent circuit

The biological properties of the cell membrane can be represented equivalently to an electric circuit, as seen in Figure 1 (Johnson & Wu, 1995).  The membrane capacitance represents the membrane dielectric property from the lipid bilayer and is totally independent of variations of permeation channels due to action potentials.  The membrane resistance represents the ion permeation through protein molecules that cross the cell membrane. Unlike the membrane capacitance, the resistance is dependent on cross-membrane voltage and time.  These cross-membrane voltage and time control the electrical signals that take place in excitable cells (Johnson & Wu, 1995).

Using the equivalent circuit representation and Kirchhoff’s laws, one can write differential equations that solve for the total flow across the membrane,, which is the sum of the capacitive current,, and the ionic current,, that flow through the channels.

2.1

As seen in equation 2.1, the sum of the currents produces a differential equation where  is the membrane potential; is the total membrane current (A/cm2);is the specific membrane capacitance (F/cm2); is the specific membrane resistance ().  The driving force of  is

The practice of representing the biological components of the cell membrane as electrical components has provided a straightforward means of calculating the capacitance of cell membranes.

Methods of Measurement

There are three methods of measurement used to find the capacitance of a cell membrane.  All methods involve insertion of two electrodes into a cell.  One electrode injects current while the other is used to measure different variables, such as voltage or current at the site of the second electrode.

Figure 2: The data plots of the Current Step Method

The first method is called the Current Step.  When a cell is in current clamp, a fixed current is injected for a certain amount of time (Iext) as shown in Figure 2. This allows the cell membrane to become fully charged as the charge is stored throughout the cell membrane. When the current is shut off the cell membrane voltages returns to rest (Vrest).  The data is plotted on a current vs. time graph as well as a voltage vs. time graph.  It is observed that the rise or decay of the voltage vs. time graph follows an exponential rise or decay.  This is due to the capacitive nature of the cell membrane.

2.2

The charging or discharging of the capacitance of the cell rises or decays with a time constant of , which is equal to the product of the resistance of the membrane () and the capacitance of the membrane (), as seen in equation 2.2.  Once  is found through fitting an exponential curve on the voltage vs. time graph, it is then divided by , which is calculated using Ohm’s Law (), to give , the capacitive value of the cell membrane.

Voltage clamp is the second type of measurement used.  This method again uses two electrodes.  With one electrode placed inside the cell, it is able to measure and compare that voltage to the voltage that is set by the experimenter on the amplifier.  The clamp amplifier then passes current back into the cell through the other intracellular electrode.  The feedback arrangement allows the membrane potential to reach the desired command voltage.  Even with constant changes due to action potentials, the voltage clamp allows the membrane potential to stay at the desired command voltage.  This method allows for the simultaneous measurement of the current needed to keep the cell at the desired voltage.  Equation 2.3 shows the mathematical steps taking in finding the capacitance of the cell through the voltage clamp:

2.3

A voltage vs. time graph, shown in Figure 3, is created and from it the change in voltage () is computed. Then a current vs. time graph is produced and there the area underneath the spike (the shaded region) is calculated

Figure 3: The data plots of the Voltage Step method

Voltage ramp is the last type of measurement that is used and is similar to the voltage clamp.  The same feedback response is used but instead of stepping the voltage to a desired value, the voltage is ramped, or held at a constant increase, until it reaches the desired voltage value and is then ramped down at the same constant decrease, as shown in Figure 4.

Figure 4 shows the resulting current vs. time graph as the voltage is ramped up and down.  It is important to note that at the onset of the ramping of voltage a slight jump downward in current() occurs and then is proceeded by a steady increase in current.  Then once the ramp direction is reversed an upward rise in current () is shown at the depth of the current vs. time graph. Finally after the voltage ramp has reached its resting value, the current jumps back down to its original value before any ramping occurred.    Just as the spike in the current vs. time graph of voltage clamp represented the capacitive nature of the cell membrane being charged, the small jumps seen in the current vs. time graph of the voltage ramp represent the capacitive nature being charged.

2.4

Figure 5: The current vs. time graph of the Voltage Ramp method

As shown in equation 2.4, that jump in current is equal to the constant value of the ramp () times the capacitance of the cell ().  A third graph is created to help visualize the jumps as a current vs. voltage graph, as shown in Figure 5.  The distance between the lines is equal to twice the ramp constant times the capacitance,.  Therefore to find the capacitance of the cell through voltage ramp, the distance between the two curves divided by twice the ramp constant yields the value of capacitance for the cell ().

Experimental

Cancer borealis crabs were purchased from Ocean Seafood (Newark, New Jersey) and were kept alive in artificial sea water tanks at 12-15° C until the experiment was conducted.  Before the experiment took place, the crabs were placed in ice for thirty minutes as a means of anesthea.  The Stomatogastric Nervous System (STNS), with the STG, was excised using standard methods (Harris-Warrick 1992).  The STNS was pinned to a Sylgard coated dish and the STG was desheathed.  The preparation was immersed in a physiological saline pH=7.4 and at a temperature range of 10-13° C.  Two microelectrodes were pulled using a Flaming-Brown micropipette puller.  One microelectrode that was used to inject current had a resistance of ~15-20Ω, while the other microelectrode that was used to measure the voltage had a resistance of ~ 25-30Ω.  As part of the procedure, the electrode injecting the current should have less resistance because too high of a resistance would impede the injected current.  Both electrodes were filled with a solution of .6M K2SO4 and 20 mM KCL.

After the STG was located through the microscope, a healthy, viable cell was chosen to be impaled.  Two electrodes would be used in the data collection; one to inject current while the other recorded the voltage.  One at a time, the electrodes were driven closer to the cell until the electrode punctured the cell membrane and a constant negative resting value was achieved.  The cell was left for a couple of minutes to ensure that the electrode was secure and would not slip out and that the normal resting value of the cell remained constant.  If everything was normal, the data collection would begin.

Using the program pClamp, ten sweeps of data was recorded per method and then averaged.  That averaged waveform was then used to find the capacitance.

For the current clamp measurements, the averaged waveform was analyzed using Clampfit.  A cursor was placed at the start of the initial rise of current and a second cursor was placed at a point along the plateau reached by the voltage after at least three time constants.  The distance between the cursors was maintained at a length chosen by the experimenter but that distance remained constant in all subsequent measurements of the current clamp.

Once the cursors were placed at the desired points along the current vs. time waveform, Clampfit was used to produce a best fit line.  Clampfit then gave a value for .  Now, only the resistance (R) is needed to solve for capacitance.  Rm was retrieved by taking the change in voltage and dividing it by the current that the experimenter injected.  With that, the capacitance of a cell membrane is computed in current clamp.

For voltage clamp waveforms, the data again was analyzed in Clampfit.  Two waveforms were recorded; a current vs. time graph as well as a voltage vs. time graph.  The benchmark for the voltage vs. time graphs is a large spike, which will be called the capacitive artifact that represents the capacitive nature of the cell membrane being charged.   As seen in the methods of measurement section, integration underneath that curve is needed to solve for the capacitance of the cell.  With the change in voltage read from the voltage vs. time graph, the capacitance can now be computed.  The area of the capacitive artifact is divided by the change in voltage, yielding the capacitive value of the cell membrane according to voltage clamp.

The voltage ramp waveforms were analyzed again using Clampfit and again a current vs. time and voltage vs. time waveform was recorded.  A graph was created to plot current vs. voltage.  Then a best fit line, in the form of , was created for each of the slant lines seen in the Figure 5.

2.5

Equation 2.5 shows the steps taken to calculate C.  Since both lines had approximately the same slope, the only variation in the two lines was seen in b.  The difference between the two b’s were taken and then divided by twice the slope of the ramp yielding the capacitance of the cell membrane according to voltage ramp.

Models

Figure 6: The first model which consists of two isopotential spheres connected by a resistive cable

Three separate mathematical models were constructed.  The first model was created modeling neurons as two isopotential cells separated by a resister as seen in Figure 6.  One isopotential cell represents the soma of a neuron while the other isopotential cell represents the dendrites found at a distance from the soma.  A cable was placed between the two compartments as a means to represent the distance between them and was given a resistance to represent the current lost as the current moves from the soma to the dendrite.

Figure 7: The second model which consists two isopotential spheres connected

by a non-isopotential, compartmentalized cylinder

After the first model was simulated, we then moved on to the second model.  The second model, shown in Figure 7, is more realistic than the first model by virtue of having a cable that not only contains a resistive value but also a capacitive value.  A real neuron connects the soma, or cell body, to the dendrites at the end of the neuron through an axon.  The axon contains a cell membrane and therefore has both resistive and capacitive qualities.  Therefore, the second model now contains a non-isopotential cable connecting two isopotential spheres.

Figure 8: The third model which consists of an isopotential sphere and two non-isopotential, compartmentalized cylinders

The third and last model is even more realistic by replacing the isopotential dendrite compartment with a non-isopotential cylinder, shown in Figure 8.  This presents a more accurate representation of the neuron because of the fact that a dendrite is long and slender and not an isopotential sphere.

Figure 9: Visual representation of current strength and movement through any compartment of a non-isopotential cylinder

By introducing compartmentalized cylinders in the second and third models, the concept of non-isopontential cells is introduced.  The compartments were indexed using j. Figure 9 shows how a typical compartment has three currents flowing in or out.  The currents are shown in equation 2.6:

2.6

The first term () and second term () reveals the current entering the jth compartment and flowing out of the jth compartment through the axial resistance (Ri), respectively.  The last term () shows the current leaving through the membrane resistance (Rm) of the jth compartment.  As shown in Figure 9, the magnitude of the current decreases through each subsequent compartment.  As a result, the voltage in each compartment is less thereby creating non-isopotential cylinders.

Mathematical Equations

2.7

The mathematical model of the voltage changes in the cell membrane are based on the differential equations seen in equation 2.7 according to Cable Theory (Rall et al., 1995).  As the models became more complex and called for indexing of compartments, equation 2.6 was added to the mathematical code of equation 2.7.  The differential program XPP (Ermentrout, 2002) was used to numerically solve the various stated equations.  The parameters that were used for each method can be seen in Table 1

Table 1: The values and parameters used for the mathematical models

In the Current Step model, the data points were plotted with a non-linear curve fit.  The data was fitted with two exponentials given by the equation 2.8:

2.8

Any number of exponentials could have been used to fit the data but two exponentials gave the most suitable fit.  The largest was found and used to solve for the capacitance as described in the Experimental Methods section.

For the Voltage Step model, the time step was extremely small due to the need for many points so that an accurate integration could take place.  The model was run and the data points were saved and imported into Matlab.  It is there that the trapezoidal method was used in finding the area underneath the current vs. time curve, the capacitive artifact.  The capacitance of the cell membrane through the Voltage Step model was calculated the same way as the experimental data was solved in the Experimental Methods section.

In the Voltage Ramp model, a step function was utilized so that the voltage would rise with a constant slope and then descended with the same constant slope.  After XPP was run with the desired parameters, a current vs. voltage graph was created.  The capacitance of the cell membrane through the Voltage Ramp model was solved exactly as was done for the experimental data as described in the Experimental Methods section.

IV. Results

Experimental

The results for the experimentally measured capacitance in eight healthy, clean recordings are shown in Table 2:

| Experiment | Current Clamp (nF) | Voltage Clamp (nF) | Voltage Ramp (nF) |
| --- | --- | --- | --- |
| 1 | 11.766 | 3.115 | 2.622 |
| 2 | 159.822 | 3.527 | 3.449 |
| 3 | 15.489 | 2.482 | 2.397 |
| 4 | 19.013 | 1.625 | 1.943 |
| 5 | 36.304 | 2.539 | 2.380 |
| 6 | 8.738 | 3.188 | 2.687 |
| 7 | 14.399 | 3.728 | 3.582 |
| 8 | 10.115 | 2.728 | 2.708 |
| Average | 34.45575 | 2.866 | 2.721 |

Table 2: The experimental results for the capacitive value of the cell membrane

for each method of measurement

From Table 2, it is clear that the current clamp measurements are extremely different to that of the voltage ramp and voltage clamp.  There is more than an 85% difference between the average voltage clamp and ramp and current clamp, while the average difference between voltage clamp and voltage ramp is approximately 5%.  A single experiment carried out all three methods of measurement on the same cell.  Therefore, all three methods should have produced approximately the same capacitance values for each method.  Voltage clamp and voltage ramp were very close to each other, while current clamp produced radically different capacitive values for the same cell.

Mathematical Models

For all of the graphs shown below, the percent actual capacitance was plotted against a change in one particular parameter.  The percent actual capacitance is the measured capacitance (as solved in the Methods section) divided by the total membrane capacitance.  Each model had its own total membrane capacitance.  The total membrane capacitance of model one is shown in equation 3.1:

3.1

Model 1 contained only two isopotential spheres and the total membrane capacitance was easily calculated with the parameters set by the experimenter.  Then each method of measurement was run for Model 1 and the membrane capacitance calculated for each method was divided by the total membrane capacitance.  That percentage illustrates how accurate the method of measurement was in calculating the actual membrane capacitance of each model.  Equations 3.2 and 3.3 show the total membrane capacitance of Model 2 and Model 3, respectively:

3.2

3.3

Refer back to Figures 6-8 for the visual representation of each model.

Model 1

To understand how the geometry of the cell affected the measured capacitance, we first varied only the diameter of the second compartment of the neuron, ddendrite of Table 1.  We ranged the ddendrite from 5 microns to 600 microns and left all other parameters the same across the three different methods.  Figure 10 reveals how much of the actual capacitive value was measured through the model as the dendrite diameter increased.

It is obvious that the Current Step method consistently stays at 100% of its actual capacitive value no matter how large ddendrite in the range given.  This shows that the Current Step is independent of the morphology of the dendrite area as an isopotential sphere.

All other methods decrease rapidly as ddendrite is increased.  It is interesting to note that the speed of the Voltage Ramp (the steepness of k) has a profound effect on the calculated membrane capacitance.  The slow Voltage Ramp (k = 0.08 V/s) produced more accurate results than the Voltage Step, while the fast Voltage Ramp (k = 4 V/s) produced worse results than the Voltage Step.  An important note is that all graphs will contain only the slow Voltage Ramp measurements from here on.

The same measurements were done again except leaving ddendrite constant at 40 microns and instead ranging lcable from 0.02 centimeters to 1 centimeter.  Figure 11 shows the relationship of the percentage of the maximum capacitance measured as the length of the cable is increased.  Again we see that the Current Step method does not change as the length is changing and stays at 100% of the actual capacitance.  The slow Voltage Ramp starts off close to 100% but trails off as lcable increases.  The Voltage Step does not even start at 100% but closer to 65% and decreases from there.  A certain arrangement will start to occur as the Current Step is the most accurate, then the slow Voltage Ramp, and then the Voltage Step.

Figure 11: The percent actual capacitance vs. cable length plot for Model 1 as lcable is increased

Model 2

For the Model 2, where the resistive cable in Model 1 has been substituted with compartmentalized non-isopotential cylinder, we ran similar simulations as in Model 1.  Figure 12 shows the effect of increasing ddendrite therefore increasing the area of the isopotential dendrite sphere.  ddendrite was ranged from 5 microns to 600 microns, which was the same range for Figure 10.  Figure 10 and Figure 12 generally follow the same curves as both ddendrite were ranged correspondingly.

Figure 13 reveals the dependence on the soma area on the percent actual capacitance.  The plot shows that there is not much of a dependence for the three methods, but the Current Step method was at 100% throughout the ranging of dsoma.  The Voltage Step and Voltage Ramp became more accurate as dsoma increased but these methods still never reached to 100% of its actual capacitance even at very large soma areas.

Figure 12: The percent actual capacitance vs. dendrite area plot for Model 2 as ddendrite is increased

Figure 13: The percent actual capacitance vs. soma area plot for Model 2 as dsoma is increased

Figures 14 and 15 show how the properties of the cable influence the calculations of the membrane capacitance.  In Figure 14, lcable is ranged from 0.02 cm to 1 cm just as in Figure 11 for Model 1, but we see for the first time that the Current Step method produces results that are not consistently at 100% of its actual capacitance.  When the parameters of the soma and dendrite were altered, it was shown that there was no effect on the Current Step method, but Figure 11 shows that there is a dependence seen as the cable length is increased.  The Current Step method decreases in accuracy as the length is increased, but it is still more accurate than the other methods.  Figure 15 shows what happens when dcable is increased.  All methods become more accurate as the diameter increases.

Figure 14: The percent actual capacitace vs. cable length plot for Model 2 as the lcable is increased

Figure 15: The percent actual capacitance vs. cable diameter plot for Model 2 as dcable is increased

Model 3

For Model 3, the isopotential sphere that represented the dendrite was changed to a non-isopotential compartmentalized cylinder.  In Figure 16, we see that increasing the dendrite diameter has very little influence on the percent actual capacitance.  The Current Step method shows little dependence on the morphology of the dendrite representation.

Figure 16: The percent actual capacitance vs. dendrite diameter plot for Model 3 as ddendrite is increased

V. Discussion

Experimental

Automatically from looking at Table 2, one would think that the Voltage Step and Voltage Ramp methods are much more accurate methods of measurement than the Current Step method, but the discrepancy seen in the abnormally large capacitive values in the Current Step is not due to the method itself, but how the data is later measured in pClamp.

As mentioned in the methods section, cursors were placed at the beginning and end of the exponential rise that were chosen arbitrarily by the experimenter.  That poses a problem because there is no universally accepted place to position the first and second cursor.  There were plenty of times where we measured the capacitance using current clamp for the same experiment but got extremely different values for , which lead to different values of capacitance.  On the other hand, voltage clamp and ramp produced precise results for the same experiment.  This raises an issue in reading current clamp results from available literature, because experimenters can perform the same exact experiments and produce different capacitive values when in fact, they are doing everything the same and should be formulating the same capacitive values.

The experimental part of this research confirmed that there was a difference in capacitance values between the three methods.  Even though in theory, they are supposed to produce the same exact results, they differed from each other.  This part of the experiment did nothing really to help prove or disprove the hypothesis, but only reaffirmed the original finding that the three methods of measuring capacitive in a cell differ greatly.  The mathematical model gives us a much better understanding and perspective in deciding if the hypothesis is supported or rejected.

Model

Figure 10 compares the percent maximum capacitance vs. dendrite diameter and shows us how accurate each method is as the dendrite diameter increases.  From there we see that, contrary to the experimental results, the Current Step method hovers around 100% maximum capacitance.  The Voltage Step and Voltage Ramp methods both drop drastically as the dendrite diameter increases.  The mechanisms concerning this have to do with how each method measures the capacitance mathematically and physically.

When a cell is injected with current, some of that current distributes along the cable and throughout the cell while some of that current is used to charge the capacitive and resistive nature of the cell (Winslow & Miller, 1989).

Figure 17: Visualization of different time constants in a non-isopotential cell

In the Current Step method, we understand that the smallest time constants found in the voltage vs. time graph correspond to the distribution of the charge throughout the cable and body of the cell.  We also know that the larger time constant refers to the time it takes for the cell membrane to charge or discharge.  That is why in the Current Step method, the fitted exponential line uses two time constants, where the smaller time constant corresponds to the distribution of charge across the cell and the other larger time constant refers to the charging of the cell membrane.  Since the capacitance of the cell membrane is the sought after value, the larger time constant should be used in all the computations to find capacitance.

The Current Step method is the only method that allows for the clear separation to be seen between the two time constants and that is why current clamp produces the most accurate result.  In the Voltage Ramp method, the current is always changing as it is being steadily increased, therefore never allowing for the equalization of the current to take place.  There is no clear distinction between the distribution of charge throughout the cell and the desired charging of the cell membrane.

The less than stellar results of voltage clamp are due to the same reasons mentioned above plus the nature of computing the capacitive artifact presented in the method.  The capacitive artifact presents a problem as computer softwares attempt to find the area underneath the curve found in Figure 3.   Computer programs integrate underneath the specified curves by approximating the area into small rectangles as seen in Figure 18.

Figure 18: Representation of basic method of numerical integration by software

The areas of the small rectangles are then added up to give an approximation of the area underneath the curve.  Unless the limit of width of the rectangles approaches zero, the area will always be an approximation and contain an error.  The combination of the sharpness of the curve plus the width of the rectangles contributes to the error already present due to the unclear separation between the larger and smaller time constants.

In Figures 11, 12, 13, and 16, the Current Step methods hover around 100% maximum capacitance as lcable, dsoma, and ddendrite are increased.   For the same reasons found above, the Current Step method proves to be very accurate over any change in those parameters because of the ability to clearly separate the two time constants.  The slow Voltage Ramp method would consistently be second in accuracy while the Voltage Clamp method would come last.

Figures 14 and 15 were the only ones where the Current Step method did change with varying parameters, but it is interesting to note that those parameters dealt with the cable length and diameter.  In Figure 14, we see that as the length of the cable increased the Current Step method’s accuracy started to decrease.  If we look at what is happening physically we might understand why this is so.  As the length of the cable is increased, the dendrites become further way from the site of measurement (the soma).  As the dendrite cell moves farther, the measurement of the capacitance decreases since our measurements become more unaware of what is happening at the end of the model.

Even though in Figure 11, the length of the cable increases but the Current Step methods stay constant at 100%, we believe it doesn’t decrease in accuracy because the cable doesn’t contain a capacitive nature, only a resistive one.  Therefore, current is lost in charging the cable and the current can get to the dendrite cell much easier.

In Figure 15, we see that he dcable is increased, which increases the Current Step method’s accuracy.  This makes sense because at very small cable diameters, we can imagine the model to be pinching off the second part of the cell model, the dendrite.  But as the diameter increases, current is allowed to flow and charge the cable and dendrite membranes allowing for accurate measurements.

It is surprising to note that the majority of all capacitance measurements are done with the Voltage Step method, which we found to be the least accurate measurement.  It is even more interesting to note that the Current Step method was developed for use in isopotential cells, but it still works effectively and correctly in non-isopotential cells.

Either way, the data from the mathematical model supports the hypothesis that the differences seen in the different methods of measurement are due to the geometry of the neuron, at least in the cases of Voltage Step and Voltage Ramp methods.  Both these methods present different capacitive values based on the diameter of the soma or dendrite compartment or by the length of the cable in between the two.  Because these two methods fail to clearly differentiate between the charging of the cell membrane and the distribution of charge throughout the cable and compartments, they provide inaccurate results that vary and depend on the specific geometry of the cells.

On the other hand, the Current Step method gives accurate results independent of the geometry of the cell due to its ability to clearly separate the two time constants.  This research supports the fact that, in theory, the Current Step method of measuring capacitance provides the most accurate results.  Precision, in contrast, is an issue that needs further research as a universal way of measuring experimental data needs to be decided upon so that a tiny change in the cursor within a fitting program does not change the calculations of , and therefore capacitance.

Further research should be done by adding branches of non-isopotential compartmentalized cylinders to Model 3.  They could be spread along the cable or bunched up as a group of fanning out at the end of the cable like the tail of a bird.  This is a more complicated model, but it is more analogous to a real neuron as the axon of the neuron has a cell membrane and therefore contains both a resistive and capacitive quality.

References

Ermentrout B. Simulating, analazing, and animating dynamical systems: a guide to XPPAUT for researchers and students (software, environment, tools). Philadelphia: Society for Industrial and Applied Mathematics, 2002.

Harris-Warrick RM, Nagy F, Nusbaum MP Neuromodulation of stomatogastric networks by identified neurons and transmitters. In: Dynamic Biological Networks: The Stomatogastric Nervous System (Harris-Warrick RM, Marder E, Selverston AI, Moulins M, eds), pp 87-138. Cambridge, MA: MIT Press. 1992

Johnson, D. & Wu, S. M.-S. (1995) Foundations of Cellular Neurophysiology (MIT Press, Cambridge, MA).

Nusbaum, M. & Beenhakker, M. A small-systems approach to motor pattern generation. Nature. 417, 343-350 (2002).

Rall, W., Segev, I., Rinzel, J & Shepherd, G.M(1995) The Theoretical Foundation of Dendritic Function: Selected Papers of Wilfred Rall with Commentaries MIT Press, Cambridge, Massachusetts

Winslow, R.L. & Miller, R.F. A theoretical and experimental study of the effects of non-uniform membrane resistance on the shape of single-cell charging curves. Neuroscience. 29, 761-771 (1989).

Acknowledgements

I would like to thank Professors Jorge Golowasch and Farzan Nadim for their patience, guidance, and dedication to us and this paper.  Also I would like to acknowledge Professor Amit Bose for his assistance throughout the project.  In addition, many thanks to Shunbing Zhao and Lakshmi Chandrasekaran for their help in the experimental and mathematical aspects for this paper.

# Text boxes

j+1

j-1

j

Soma

Dendrite

Soma

Figure 4: The data plots of the Voltage Ramp Method

Dendrite

Rm

Rm

Rm

Ri

Ri

m

Figure 10: The percent actual capacitance vs. dendrite diameter plot f or Model 1 as ddendrite is increased

ic=2kC